## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
By Yan Zhuang
YASC
GitHub

## Slide 2: Introduction
The goal of the project is to develop an interactive recorder performance tool, incorporating Joy-Con controllers via a web interface for gesture-based inputs and SuperCollider for sound synthesis.

## Slide 3: SuperCollider
It's an engine for sound synthesis and algorithmic music composition.
It's a real-time sound-based OOP language.
https://supercollider.github.io

## Slide 4: Joy-Con controller
Primary controllers for the Nintendo Switch gaming console.
We could use that to play music.

## Slide 5: Structure overview
User interaction accomplished with Joy-Con controllers.
Web system acts as main interface.
SuperCollider serves as sound synthesis engine, generating/editing sounds according to the web system commands sent via OSC protocol.
Sound captured by the web system to provide visual feedback.

## Slide 6: Web system – Map your controller
Through this page, Joy-Con controller can be mapped to different functions.
The left controller is responsible for adjusting parameters in SuperCollider.
The right controller is dedicated to play notes.

## Slide 7: Web system – Train your memory
The dino game page is an interactive training tool designed to help users familiarize with their custom hotkeys.
If you want to jump, press the corresponding hotkey.

## Slide 8: Web system – Play recorder
The performance page provides an immersive audio-visual experience by showing the output sound spectrum.

## Slide 9: Web system – Implementation
There are three main components which run the web system:

## Slide 10: Sound synthesis – GUI
The recorder sound produced in SuperCollider. Users can see the changes made with controllers of some parameters:
Amplitude envelope attack and release time.
Vibrato frequency and depth.
Reverb D/W mix, time and pre-delay.

## Slide 11: Sound synthesis – Implementation
Perry Cook’s recorder model

## Slide 12: Future work
Implement features that allow users to record, save, and replay their performances.
The waveguide model doesn’t behave well at high frequencies. In the short future, multi-modal or multi-dimensional models could be adopted to solve the issue.
Offer more sophisticated sound parameters for users to control in SuperCollider.

## Slide 13
Thanks